## Slide 1
Module 6: Sludge Management
ECAM Tool:
Energy performance and Carbon emissions Assessment and Monitoring tool

## Slide 2
Interrelation of climate change and the water cycle
Typical emission sources of drinking water and wastewater utilities
Purpose of initial and detailed assessment
Purpose baseline report and important factors for assessing PIs
Link between ECAM, baseline report and WaCCliM Roadmap
RECALL
Module 6: Sludge Management

## Slide 3
WaCCliM Roadmap
Module 6: Sludge Management

## Slide 4
Relate sludge management processes to climate change and mitigation
Apply ECAM tool to assess baseline performance
Simulate and compare scenarios to improve sludge management
LEARNING OBJECTIVES
Module 6: Sludge Management

## Slide 5
SLUDGE MANAGEMENT IN A NUTSHELL
Residual, semi-solid by-product material from WWTPs
Related operations can add up to 50% of total operation costs
Risks for pathogenic microorganisms
Treatment goals: reduce volume and costs, reuse
Sludge management relates to all operations aiming at treating sludge that is produced in WWTPs
Module 6: Sludge Management

## Slide 6
SLUDGE MANAGEMENT IN A NUTSHELL
Two types of processes are distinguished:
Primary and secondary inside the fence of the WWTP for energy production or feedback processes
“Waste” Sludge is disposed of, thus outside the fence, overstepping the boundaries of the WWTP
INSIDE THE FENCE
OUTSIDE THE FENCE
INSIDE VS OUTSIDE FENCE
FOCUS IN ECAM V2.0 IS ON DIRECT GHG EMISSIONS INSIDE AND OUTSIDE THE FENCE
Module 6: Sludge Management

## Slide 7
SLUDGE MANAGEMENT IN A NUTSHELL
INSIDE THE FENCE
Primary Clarification
Biological Treatment
Secondary Clarification
Thickening
Dewatering
Storage
Digestion
Incineration
Disposal
Settling tanks for continuous removal of solids
Reactors employing microorganisms to break down organic matter
Water removal from sludge
Removal of flocs created during certain biological treatments
Increase of the sludge density
Anaerobic treatment of sludge
Thermal destruction of sludge
Storage before further treatment steps
Final destination of the waste product
UNIT PROCESS DESCRIPTION
EFFECTS
Reduce BOD Load
Reduce TSS Content
Reduce BOD/nutrient Load
Reduce TSS Content
Reduce Sludge Volume
Increase Solid Fraction
Reduce BOD Load
Reduce TSS Content
Reduce Sludge Volume
Refine Sludge Structure
Reduce BOD Load
Reduce Volume
Reduce Volume
SIMPLIFIED PROCESSES OF WWTP
Module 6: Sludge Management

## Slide 8
IMPACT ON CLIMATE CHANGE
WHAT’S THE LINK?
  Sludge is produced as a waste material in WTTPs
  Sludge management requires energy, thus emitting CO2 at different steps
  Choice of disposal technique greatly affects the amount of emissions
  Choice of handling and ultimate disposal techniques determine opportunities for resource recovery and minimized GHG emissions
  When possible, it is crucial to implement reuse and resource valorization
SLUDGE AS A RESOURCE RATHER THAN WASTE
SLUDGE MANAGEMENT OPERATIONS
GHG EMISSIONS
Module 6: Sludge Management

## Slide 9
IMPACT ON CLIMATE CHANGE
PROCESSES
Primary Clarification
Biological Treatment
Secondary Clarification
Thickening
Dewatering
Storage
Digestion
Incineration
Disposal
EMISSIONS in ECAM V2.0
TYPICAL EMISSIONS FOR SINGLE PROCESSES
CH4
CH4, CO2 (included in kWh consumed by WWTP)
CH4
N2O
CO2 (included in kWh consumed by WWTP)
CH4
N2O
CO2 from transportation to disposal
CO2 (included in kWh consumed by WWTP)
N2O, CO2 (included in kWh consumed by WWTP)
Module 6: Sludge Management

## Slide 10
IMPACT ON CLIMATE CHANGE
SLUDGE MANAGEMENT AND THE URBAN WATER CYCLE
Adopting a holistic approach to improve sludge management…
Module 6: Sludge Management
Notes: The holistic approach is relevant when assessing sludge management (e.g. Relation digestion and sludge volume that requires treatment, impact on emissions of reduced inflow and infiltration)

## Slide 11
ASSESSING GHG AND ENERGY PERFORMANCE
  First, let's understand distinction between non-digested and digested sludge
digested sludge
Less volume
Less carbon content
non-digested sludge
More volume
More carbon content
Module 6: Sludge Management

## Slide 12
ASSESSING GHG AND ENERGY PERFORMANCE
  Sludge production estimation versus actual numbers in detailed assessment
    Assumes 4% solids in waste sludge for dry weight calculation
    70% volatile solids for non-digested
    51% volatile solids for digested
  Select disposal method
Tier A - Initial GHG Assessment in ECAM
Module 6: Sludge Management

## Slide 13
ASSESSING GHG AND ENERGY PERFORMANCE
  Sludge production based on actual numbers:
    However, if sludge wet and dry weight are not known:
      Assumes 4% solids in waste sludge for dry weight calculation; however, if centrifuge and/or chemical condition specified, 20% solids is assumed.
    70% volatile solids for non-digested
    51% volatile solids for digested
  Disposal Method
    Now can choose any combination of methods, not just one as for initial assessment
    Differentiates between coarse-textured and fine-textured soils for Land Application
    Activity info for emissions from truck transport now specified
  Sludge storage methane emissions now accounted for if there is storage
Tier B - Detailed GHG Assessment in ECAM
Module 6: Sludge Management

## Slide 14
ASSESSING GHG AND ENERGY PERFORMANCE
Module 6: Sludge Management

## Slide 15
OPPORTUNITIES
MITIGATION OF EMISSIONS
  Inside fence - Improve energy efficiency and biogas production/valorization to reduce kWh & GHG emissions
  Outside fence - Taking advantage of opportunities for alternate disposal options that allow resource recovery and cause less GHG emissions:
ANAEROBIC DIGESTION
SLUDGE DISPOSAL
INCINERATION
Landfill Gas recovery
Nutrient recovery
(composting, land application)
Heat recovery
Biogas valorization
SLUDGE DISPOSAL
Module 6: Sludge Management

## Slide 16
OPPORTUNITIES
MITIGATION OF EMISSIONS
  Potential to reduce emissions depends on improvement measure
  Examples Utility A – 30,591 kg (dry weight) sludge per year
Composting and Land Application Overall emission reduction of up to 93% compared to landfilling Main differences: emission factors and resource recovery
Take home: Landfill with biogas recovery is best option since there would be no methane emissions
Module 6: Sludge Management
Notes: Land application: Emissions factors vary according to the soil typology. ECAM differentiates between coarse-textured and fine-textured soils.

## Slide 17
EXERCISE: COMPARING EMISSIONS
LEARNING EXERCISE
Picture a hypothetical municipal wastewater treatment plant.
Match each unit process with its likely emission value.
Assume a primary sludge mass of 30 tons and a biogas production of 20000 m3. Amount of biogas flared is 5000 m3
Refer to equations in manual
Process
Storage 5 days - CH4
Incineration - CH4
Flaring - CH4
Landfilling - CH4
Composting - CH4
Emissions [kg]
40
5500
1
500
2000
Module 6: Sludge Management

## Slide 18
How does sludge management contribute to climate change?
Difference inside and outside the fence processes, and link holistic urban water cycle approach
  Resource recovery by land application/composting
  Biogas production and valorization (inside and outside)
4 key improvement measures and their relative impact
RECAP
Module 6: Sludge Management